THE APC-22 FORM IS NOT TO BE USED FOR FILING A TITLE V OPERATING PERMIT APPLICATION

INSTRUCTIONS

EMISSION POINT DESCRIPTION (APC 22)

This form should be completed for each stack or other clearly defined point of pollutant emissions within the source.

Line 1. -	The right-hand portions of the first two lines are intended for APC Division use only,

Line 2. -	The process Emission Source Number should be the same as entered in Item 5 of the permit

application for (APC 20).  The Flow Diagram Point number should be a code that will reference the

emission point in question to the process flow diagram accompanying this application.

Line 3. -	Location of the emission point should be entered in either latitude & longitude to the nearest

seconds, or UTM coordinates to the nearest .01 kilometer.  For example 495.27 and 3948.61 are

UTM horizontal and vertical coordinates respectively.

Lines 5.-6. -	Complete these items only if the operational schedule of this emission point differs from the

overall source operational schedule as entered in Items 4 & 5 of the Source Description Sheet

(APC 21).

Line 8. -	Emission estimates for each pollutant emitted from this point should be based on stack sampling

results or engineering calculations.  In certain cases other estimates may be accepted.  Average

emissions (lbs/hr) should be representative of the following:

a.	For continuous or long-run, steady-state, operations it is the total weight of pollutant emitted to

the atmosphere for the entire period of continuous operation or for a typical portion thereof

divided by the number of hours of such period or portion thereof.

b.	For cyclical or batch type operation, it is the total weight of the pollutant emitted to the

atmosphere for a period which covers a complete or an integral number of cycles divided by the

hours of actual process operation during such periods.

Maximum emissions (lbs/hr) should be determined by dividing the total highest emissions possible

during any 3 hour period with control equipment working properly, by 3.  This will be dependent

upon such things, either singly or in combination, as maximum possible operating rate, a particular

input material, product, or fuel which may result in increased emissions; periods of highest

emissions for cyclical or batch type operations, etc.  Concentrations should be determined for stack

emissions only and should reflect average exit gas concentrations reported in the units specified on

the Description  Form.

Emission estimation method and control device descriptions, along with corresponding codes, can be found on the back of the Permit Application Form (APC 20).  The codes which most accurately describe the estimation methods and control equipment used, along with the estimated control equipment efficiency should be entered for each pollutant present.  Any estimation methods of control devices other than those listed in the tables should be described in the comments (Item 10).

Line 11. -	Unsigned and/or undated applications will not be processed.